## Slide 1: UM User Meeting 2018
考虑轮对柔性的车辆-道岔耦合动力特性分析
Analysis of Vehicle-Turnout Coupling Dynamic Characteristics
Considering Wheelset Flexibility
October 25, 2018
Vehicle-Turnout Coupled Dynamics
Email: jiayin_chan@163.com
西南交通大学，高速铁路线路工程教育部重点实验室
徐井芒，陈嘉胤
Southwest Jiaotong University, Key Laboratory of High-speed Railway Engineering, Ministry of Education
Jingmang Xu, Jiayin Chen

## Slide 2: 汇报提纲 Outline
背景与问题 Background and problems
计算模型 Calculation Model
计算案例 Case study
总结与展望 Conclusion and future work
道岔动力学计算快速化
车辆-道岔耦合动力学模型
模型验证
岔区轮轨动态相互作用
柔性轮对
Vehicle-Turnout Coupled Model
Flexible Wheelset
Model validation
Wheel-rail interaction in turnout
Rapid computation requirement of turnout dynamics

## Slide 3: 背景与问题 Background and Problems
道岔动力学计算快速化 Accurate calculation of turnout dynamics
钢轨廓形演变
入岔姿态
轨下结构刚度
几何不平顺
车轮凹磨
车轮多边形化
其他轮轨损伤
…
激励
动力学模型
多刚体动力学模型
有限元模型
刚柔耦合模型
评价指标
道岔动力破坏作用
岔区行车品质
随机分析
敏感性分析
概率密度演化理论
轮轨关系修复
Excitation
Random analysis
随机取样方法
Dynamic model
Evaluating indicators

## Slide 4: 计算模型 Calculation Model
柔性轮对 Flexible wheelset
CRH380B高速列车轮对，S1002CN踏面
Wheelset of CRH380B high-speed trains, S1002CN tread
f (2, 3) = 107.03Hz
第一阶轮对弯曲
f (4, 5) = 183.67Hz
车轮反对称偏转
f (7, 8) = 343.81Hz
车轮对称偏转
f (14, 15) = 645.83Hz
第二阶轮对弯曲
f (19, 20) = 1122.22Hz
第四阶轮对弯曲
f (28, 29) = 1780.1Hz
第六阶轮对弯曲
f (16, 17) = 870.45Hz
第三阶轮对弯曲
f (26, 27) = 1514.80Hz
第五阶轮对弯曲
3rd order wheelset bending
4th order wheelset bending
5th order wheelset bending
6th order wheelset bending
1st order wheelset bending
2nd order wheelset bending
Wheel antisymmetric deflection
第一类：轮对弯曲变形
Group 1: Bending deformation of wheelset
Wheel symmetric deflection

## Slide 5: 计算模型 Calculation Model
柔性轮对 Flexible wheelset
350Hz以下模态以轮轴变形为主，中高频模态以车轮的辐板和轮辋变形为主
第二类：轮辐伞形变形
Group 2: Umbrella shape deformation of spoke
f (9-12) = 445.92Hz 2节径车轮变形
(节径数m, 节圆数n, 节径1~m与X轴夹角)
(2, 0, 45, 135) symmetric
(2, 0, 0, 90) antisymmetric
f (6) = 306.57Hz 一阶对称伞形
f (21-24) = 1148.35Hz 3节径车轮变形
(3, 0, 0, 60, 120) symmetric
(3, 0, 30, 90, 150) antisymmetric
f (13) = 459.04Hz 一阶反对称伞形
1st order symmetric
1st order antisymmetric
第三类：车轮变形
Group 3: Wheel deformation
(Number of Nodal diameter m, Number of Nodal circle n, Angle between nodal diameter 1~m and X axis)

## Slide 6: 计算模型 Calculation Model
柔性轮对 Flexible wheelset
Displacements of the points are computed by interpolation of the corresponding values of the neighboring nodes
基于拉格朗日方法确定滚动接触踏面运动学关系
The profile kinematics in rolling contact is determined by Lagrange approach.
The profile is also assumed to be non-deformable but its position and orientation are computed taking into account displacements of points on the wheel rolling surface.
刚性踏面，其位置和方向考虑车轮滚动接触表面附近节点位移
181,440 solid 45 elements and 2 interface nodes in FEM platform

## Slide 7: 计算模型 Calculation Model
车辆-道岔耦合动力学模型 Vehicle-Turnout Coupled Model
转辙器区 Switch panel
辙叉区 Crossing panel
道岔廓形 Turnout profile
车辆模型拓扑图 Topological graph of vehicle model
移动惯性道岔模型，K-P算法
Moving inertial turnout model, K-P approach.
CRH380B
High-speed Vehicle
350 km/h CN60-1100-1:18 turnout

## Slide 8: 计算案例 Case study
模型有效性验证 Model validation
[1] Wu X, Rakheja S, Ahmed A, et al. Influence of a flexible wheelset on the dynamic responses of a high-speed railway car due to a wheel flat[J]. Journal of Rail & Rapid Transit, 2017, 232(4).
无激励条件下，轮轴弯曲应力变化
Bending stress evaluation of the axle shaft without excitation.
X.W. Wu, S. Rakheja, AKW Ahmed, et al.[1]
4×0.030 s
Lateral bending stress of axle shaft
轮轴横向弯曲应力
350km/h
100km/h

## Slide 9: 计算案例 Case study
模型有效性验证 Model validation
在垂向激励下，轮轨横向力相对轮轨垂向力受轮对弯曲模态影响更大。
The bending mode of wheelset has greater effect on the lateral wheel-rail force than the vertical one under the vertical excitation.
fu1
fb2-XOY
fn2, fu1-anti
fb2-YOZ
fIrr-1
10-1
1
102
1
102
10-2
101
103
10-2
10-1
101
103
2fIrr
2fIrr
Unit：N
轮轨横向力 Lateral wheel-rail force
轮轨横向力最大值 Max. Lateral wheel-rail force
320km/h, 444Hz
220km/h,
305Hz
fu1
fb2
1阶对称伞形变形
2阶弯曲变形
250km/h
350km/h

## Slide 10: 计算案例 Case study
0.065m
1.944m
PSD
模型有效性验证 Model validation
白噪声垂向不平顺激励 ( f = 50~1500Hz, A = 0.02mm) 条件下轮轨力在频域内变化
Wheel-rail force in frequency domain under white noise vertical irregularity excitation ( f = 50~1500Hz, A = 0.02mm) .
Time domain
白噪声垂向不平顺激励
White noise vertical irregularity excitation
轮轨力频域图
Wheel-rail force in frequency domain
Lateral
Vertical

## Slide 11: 计算案例 Case study
岔区轮轨相互作用 Wheel-rail interaction in turnout
柔性轮对轮轨垂向力最大值显著减小，辙叉区减小了8.6%
The vertical wheel-rail force significantly decreases by 8.6% in crossing panel for flexible wheelset.
尖轨侧轮轨垂向力
转辙器区
Vertical wheel-rail force at switch rail side
Switch Panel
辙叉区
Crossing Panel
Notes: 考虑到车辆高速运行时，在无激励的状态下，轮对运动以50Hz以下的旋转频率为主。为了扩大激励频率的分析范围，对模型施加了由频率范围为50~1500Hz、幅值为0.02mm的白噪声生成的垂向不平顺激励，由它的功率谱密度图可知，其幅值较大的波长范围在0.065m~1.944m。如右图所示，在白噪声激励下，柔性轮对轮轨垂向力幅值差别不大，而对结果进行时频转换分析，可知柔性轮对轮轨垂向力在旋转频率36Hz及其倍数中出现了峰值；同时，它也激起了轮对在ZOY平面内第3阶弯曲频率。
对其结果进行快速傅里叶变换，可知在频域中，柔性轮对模型的结果体现出的频率成分更加丰富轮轨横向力除了在对应旋转运动频率出现局部峰值以外，对在XOY平面内第1阶、第2阶 、第4和第6阶轮对弯曲变形模态处均出现了峰值。相比于轮轨垂向力，考虑轮对弹性对轮轨横向力的影响更显著。

## Slide 12: 计算案例 Case study
岔区轮轨相互作用 Wheel-rail interaction in turnout
柔性轮对车轮垂向位移增大，减小了垂向接触刚度
For flexible wheelset, the vertical displacement of wheel increases that decreases the vertical contact stiffness.
尖轨侧车轮名义滚动圆处垂向位移
Vertical displacement of wheel nominal rolling circle at switch rail side
(a) 转辙器区
Switch Panel
(b) 辙叉区
Crossing Panel

## Slide 13: 计算案例 Case study
岔区轮轨相互作用 Wheel-rail interaction in turnout
柔性轮对所得轴箱垂向加速度频域结果更贴合实测结果
The frequency domain results of vertical acceleration of axle box obtained from flexible wheelset are more consistent with the measured results.
轴箱垂向加速度
Vertical acceleration of axle box
450~650Hz
实测轴箱垂向加速度[2]
Measured vertical acceleration of axle box
350~600Hz
47Hz
[2] 任尊松, 刘志明. 高速动车组振动传递及频率分布规律[J]. 机械工程学报, 2013, 49(16):1-7.
320 km/h
350 km/h
Notes: 转辙器：30mm，辙叉：40mm

## Slide 14: 计算案例 Case study
岔区轮轨相互作用 Wheel-rail interaction in turnout
柔性轮对横向蠕化率增大，接触斑更接近饱和
For flexible wheelset, with the increase of transverse creepage, the contact patch are closer to saturation.
尖轨侧车轮横向蠕化率
Lateral creepage of wheel at the switch rail side

## Slide 15: 总结与展望 Conclusion and future work
总结 Conclusion
柔性轮对所得轴箱垂向加速度频域结果贴近实测高速道岔激振范围
The frequency domain results of vertical acceleration of axle box obtained from flexible wheelset are more consistent with the measured results.
柔性轮对增大横向蠕化率
Flexible wheelset increases the transverse creepage
柔性轮对减小轮轨垂向接触刚度并降低8.6%轮轨垂向力最大值
Flexible wheelset decreases the vertical wheel-rail contact stiffness that decreases the maximum vertical wheel-rail force by 8.6%.
柔性轮对弯曲模态增强了系统横向动力响应
The bending modes of flexible wheelset enhances the lateral response of system.
Notes: 转辙器：30mm，辙叉：40mm

## Slide 16: 总结与展望 Conclusion and future work
展望 Future work
轮轨接触算法：考虑尖轨与基本轨、心轨与翼轨的相对运动
Considering the relative motion between switch rail and stock rail as well as nose rail and wing rail in the wheel-rail contact approach.
道岔区中车辆牵引、制动时道岔系统纵向动力响应
Longitudinal dynamic response of turnout system with vehicle traction and braking.
Notes: 转辙器：30mm，辙叉：40mm

## Slide 17: UM User Meeting 2018
考虑轮对柔性的车辆-道岔耦合动力特性分析
Analysis of Vehicle-Turnout Coupling Dynamic Characteristics
Considering Wheelset Flexibility
October 25, 2018
Vehicle-Turnout Coupled Dynamics
Email: jiayin_chan@163.com
Thank you and questions welcome
感谢聆听，欢迎您的提问