## Slide 1: Roman Kovalev
Recent Advances in Universal Mechanism Software and Finished Projects
Presenter: Dr. Roman Kovalev
Laboratory of Computational Mechanics
Bryansk State Technical University

## Slide 2: Contents
Recent Advances in Universal Mechanism Software
  New tool for predicting wear of railway wheel profiles
  Renewed UM RCF tool
  New tool for simulation of pantograph-catenary interaction
  New graphical engine
Recently finished projects
  Optimization of wheel profiles: dynamics, wear and rolling contact fatigue
  International benchmarking of longitudinal train dynamics simulators
  Train simulator
Conclusion

## Slide 3: The parallel discrete approach to wear modeling
Scheme of wear simulation
n
1
2
3
n – number of wear steps

## Slide 4: The parallel discrete approach to wear modeling
The "Parallel" means that different configurations of rail vehicles are modeled in parallel, with the same wheel profiles for all configurations. Configurations differ in track macrogeometry, track irregularities, vehicle mass and so on. The set of configurations should be a representative set of conditions in which the rail vehicle is operated.
The "Discrete" means that the track length traveled by the vehicle during the simulation is divided into a sequence of intervals (wear steps). The number of intervals is the same for all configurations. Within each interval the profiles are not changed. At the end of each wear step, a wear depth is scaled according to a mileage assigned to one wear step. After scaling, the wear depth is summarized for the respective wheels by taking into account the weight (statistical) factors of the configurations and the wear symmetry, if any. Then the profiles are updated according to accumulated wear depth.

## Slide 5: Wheel/rail contact models for wear simulation
Contact model by W. Kik and J. Piotrowski + FASTSIM algorithm;
CONTACT library.
Example of a multi-point non-Hertzian wheel/rail contact

## Slide 6: Wear models
Archard model
where is the volume wear [m3];
is the wear coefficient [m3/J];
is the work of frictional forces [J].
where is the power of frictional forces [W].
where is the tangential traction [Pa];
is the sliding velocity [m/s];
is the contact patch area [m2].
While using the FASTSIM-like algorithms, the work of frictional forces is calculated according to the following formula:
where is the wheelset velocity [m/s];
is the integration time step size [s]
is the creep [-].
x
y

## Slide 7: Wear models
Specht model
where is the critical power density of frictional forces [W/m2];
is the jump coefficient [-].
A [J/ mm2]
mild wear regime
W [μg/ mm2]
severe wear regime

## Slide 8: Profile-updating procedure
Wear mask
before wear step
Histogram of distribution of volume wear
after wear step
wear step
1
Accumulation of volume wear for every separate wheel of a wheelset

## Slide 9: Profile-updating procedure
2
Taking into account the symmetry of wear
Symmetrical wear of wheel profiles of same wheelset
where , is the volume wear for the left and the right wheels of the wheelset calculated for the configuration at motion with speed .
Symmetrical wear of wheelsets
where is the number of wheelsets.
3
Scaling volume wear according to a mileage assigned to one wear step
4
Sum of volume wear for every wheel
where is the weight of configuration;
is the weight of speed;
is the number of configurations.

## Slide 10: Profile-updating procedure
5
Calculation of wear depth in the center of each circumferential strip
where is the smoothed volume wear;
is the arc-coordinate of the center of the strip ;
is the wheel radius;
is the width of wear accumulation interval.
6
Profile updating
where is the external normal for the wheel profile.

## Slide 11: UM Loco/Wheel Profile Wear Evolution tool

## Slide 12: Contents
Recent Advances in Universal Mechanism Software
  New tool for predicting wear of railway wheel profiles
  Renewed UM RCF tool
  New tool for simulation of pantograph-catenary interaction
  New graphical engine
Recently finished projects
  Optimization of wheel profiles: dynamics, wear and rolling contact fatigue
  International benchmarking of longitudinal train dynamics simulators
  Train simulator
Conclusion

## Slide 13: UM Rolling Contact Fatigue
Renewed UM RCF has the following new features:
now four RCF criteria for modeling of the accumulation of RCF damage are available:
  Dang Van criterion;
  maximum shear stress;
  Sines criterion;
  combined criterion;
UM RCF now supports UM Loco/Wheel Profile Wear Evolution tool;
steel hardness is now taken into account;
residual stresses are now taken into account.

## Slide 14: RCF curves
Weller's type of curves are used for calculation. RCF curves for different criteria and steel hardness 255–330 HB are shown below.

## Slide 15: Contents
Recent Advances in Universal Mechanism Software
  New tool for predicting wear of railway wheel profiles
  Renewed UM RCF tool
  New tool for simulation of pantograph-catenary interaction
  New graphical engine
Recently finished projects
  Optimization of wheel profiles: dynamics, wear and rolling contact fatigue
  International benchmarking of longitudinal train dynamics simulators
  Train simulator
Conclusion

## Slide 16: UM Catenary to be released in the beginning of 2019
In 2018 we have started the development of a new module UM Catenary

## Slide 17: Pantograph-Catenary interaction software
(1) DB – DB Systemtechnik GmbH (PrOSA), Germany; (2) IST – Instituto Superior Tecnico Lisboa (PantoCat), Portugal; (3) KRRI – Korea Railroad Research Institute (SPOPS), Republic Korea; (4) KTH – Royal Institute of Technology (CaPaSIM), Sweden; (5) POLIMI – Politecnico di Milano (PCaDA), Italy; (6) RTRI – Railway Technical Research Institute (Gasen-do FEM), Japan; (7) SNCF – Societé Nationale des Chemins de Fer (OSCAR), France; (8) SWJTU – Southwest Jiaotong University (PCRUN), People’s Republic of China; (9) UPCo – Universidad Pontificia Comillas de Madrid (CANDY), Spane; (10) UPV/TALGO – Universitat Politècnica de València & TALGO S.L. (PACDIN), Spane.
World-wide scientific activities in simulation of railway catenary system dynamics benchmarking:
Stefano Brunia, Jorge Ambrosiob, Alberto Carniceroc, Yong Hyeon Chod, Lars Finnere, Mitsuru Ikedaf, Sam Young Kwond, Jean-Pierre Massatg, Sebastian Stichelh, Manuel Turi and Weihua Zhang. The results of the pantograph–catenary interaction benchmark. Vehicle System Dynamics, 2015, Vol. 53, No. 3, Pages 412–435.

## Slide 18: UM Catenary
Types of railway catenary systems to be implemented:
Simple
Switched
Compound

## Slide 19: Model of 3D catenary system
Main elements:
Messenger wire: pre-tensioned geometric nonlinear beam elements
Contact wire: pre-tensioned Timoshenko beam FE
Droppers: bipolar force elements

## Slide 20: Analysis of catenary systems
Tests:
Equilibrium of catenary system
Given vertical positions of contact wire at dropper locations and wire tensions
Dynamic analysis of pantograph-catenary system interaction
Pantograph only
Complete 3D model of locomotive

## Slide 21: Equilibrium test
Example: 4 spans, 220 meters, 80 geometrically nonlinear FE
Equilibrium computation by integration of motion equations
Simulation is 10 times faster than real time

## Slide 22: Contents
Recent Advances in Universal Mechanism Software
  New tool for predicting wear of railway wheel profiles
  Renewed UM RCF tool
  New tool for simulation of pantograph-catenary interaction
  New graphical engine
Recently finished projects
  Optimization of wheel profiles: dynamics, wear and rolling contact fatigue
  International benchmarking of longitudinal train dynamics simulators
  Train simulator
Conclusion

## Slide 23: New graphical engine – beta version is available to download
Beta-testing: UM 8.5 now includes UM Simlation program based on a new graphical engine.
+ New graphical engine provides 5-100 times higher frame rate + It effectively supports all modern video cards including ATI Radeon + More user friendly basic operations: move, rotate, zoom + Instant rotation center is used. Rotation is allowed around any arbitrary point.
+ Accurate detection of 3D coordinates under the mouse cursor + Video recording works correctly even if the recorded window is overlapped by any other windows + Transparent objects are now supported + List of Cameras is introduced + Image modes (wired, solid, transparent, invisible) are now available for all model elements, not for bodies only

## Slide 24: Contents
Recent Advances in Universal Mechanism Software
  New tool for predicting wear of railway wheel profiles
  New tool for simulation of pantograph-catenary interaction
  New graphical engine
Recently finished projects
  Optimization of wheel profiles: dynamics, wear and rolling contact fatigue
  International benchmarking of longitudinal train dynamics simulators
  Train simulator
Conclusion

## Slide 25: Purpose of the research
Classical three-piece bogie of 18-100 type
New three-piece bogie design: 18-9855 type
Choice of rational wheel profiles for
freight car with a three-piece bogie type 18-100;
freight car with a three-piece bogie type 18-9855;
passenger cars.
Bogie of the passenger car

## Slide 26: Approach
Car model
Loaded car
R=350 m
R=650 m
Tangent
Empty car
New car
Worn car
New rail
Worn rail
120 km / h
20 km / h
30 km / h
Wear life
Derailment
RCF
Wear factor
Lateral forces
Profile 1
Profile 2
Operating conditions
Performances
Alternatives
Computer simulation using "Universal Mechanism“ Software
The choice of profile is a multicriterion problem of finding solutions considering a set of operating conditions of the profile.
General criterion is based on an estimation of wheel profile life due to wear and rolling contact fatigue.
Particular (secondary) criteria:
wear intensity of profiles;
lateral wheel-to-rail forces;
Safety factor L/V.
Notes: The choice of the optimal profile in this case is considered as a choice among a given initial set of alternative profiles using several criteria and taking into account the multitude of operating conditions of the car.
The choice of the initial set of profiles in this case is not discussed.
A brief overview of the methods for selecting initial profiles can be found, for example, in Enblom R: Simulation of Wheel and Rail Profile Evolution - Wear Modelling and Validation. TRITA -AVE Report 2004:19, Division of Railway Technology, Department of Aeronautical and Vehicle Engineering, Royal Institute of Technology (KTH), Stockholm 2004
Secondary criteria (lateral forces and the derailment coefficient L/V) are used as constraints in the choice of alternative. Basic profiles selection criteria were Wear and Rolling Contact Fatigue (RCF).
In this study we used a railroad track model with an inertial rail and a contact model of V. Kick and I. Piotrovsky.

## Slide 27: Wear estimation
Wear estimation
is performed in the evolution of wheel profiles
Two wear indicators for the wheel profile
Tread wear;
Flange wear.
Evolution of the profile
It allows us to estimate intensity of wear of different areas of the wheel profile during the operation.
Chart: Mileage, thous.km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Tread | 0 | 0.25 | 0.44 | 0.59 | 0.73 | 0.88 | 1.05 | 1.21 | 1.36 | 1.51 | 1.65
Flange | 0 | 1.39 | 2.06 | 2.53 | 2.93 | 3.19 | 3.36 | 3.55 | 3.7 | 3.85 | 3.99
Notes: In particular, on the lower graph you can see that the wear rate of the flange varies while the wear rate of the tread is constant. At the end of the run, the wear rate of the flange and tread becomes approximately equal.
These results are obtained for a freight car on three piece bogies with standard conical wheel profiles. This car serves as a basis for comparison.

## Slide 28: Optimal profile for freight cars – P5
Optimal profile P5
has significant advantages in terms of wear in comparison with the standard conical profiles (GOST 10791). The resource for the wear of the flange is increased by 120 -140 thousand km, and for the wear of the rolling surface by 25-30 thousand km.
Chart: Mileage, thous.km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Standard | 0 | 1.39 | 2.06 | 2.53 | 2.93 | 3.19 | 3.36 | 3.55 | 3.7 | 3.85 | 3.99
P5 | 0 | 0.17 | 0.42 | 0.68 | 0.92 | 1.15 | 1.38 | 1.59 | 1.8 | 2 | 2.19
140 thous. km.
Chart: Mileage, thous.km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Standard | 0 | 0.25 | 0.44 | 0.59 | 0.73 | 0.88 | 1.05 | 1.21 | 1.36 | 1.51 | 1.65
P5 | 0 | 0.09 | 0.23 | 0.38 | 0.54 | 0.69 | 0.85 | 1 | 1.15 | 1.3 | 1.45
Standard
Standard conical profiles
P5
Optimal profile
Notes: These results are obtained for a freight car on three piece bogies with standard conical wheel profiles ГОСТ (as a basis for comparison) and optimal profile P5 .

## Slide 29: Profile P5. Estimation of fatigue life
The evaluation of Contact Rolling Fatigue is performed using the UM RCF module, the initial data for which are accumulated during the calculation of evolution. Thus, the affect of profile wear on accumulation of contact fatigue damages is taken into account.
Rolling Contact Fatigue is calculated simultaneously with wear. So the most damaged particles close the surface are removed by the wear.
Chart: Mileage, thous.km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Standard | 0 | 0.113 | 0.239 | 0.37 | 0.485 | 0.578 | 0.658 | 0.732 | 0.813 | 0.901 | 1
P5 | 0 | 0.064 | 0.096 | 0.159 | 0.241 | 0.339 | 0.445 | 0.561 | 0.675 | 0.794 | 0.921
Notes: The P5 profile provides greater fatigue durability than the standard conical profile.

## Slide 30: Profile P5. Checking dynamical restrictions
At all stages of evolution, the most important dynamic indicators for the most dangerous modes of motion were checked.
Lateral wheel-to-rail forces when the loaded car is moving with the maximum permitted speeds.
Safety factor (used in Russia inverse Nadal's derailment criterion) for an empty car at the maximum permitted speed.
Chart: Mileage, thous. km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Standard | 71.71 | 62.56 | 75.66 | 61.3 | 67.93 | 74.07 | 73.78 | 73.37 | 72.05 | 79.07 | 78.5
P5 | 78.22 | 77.97 | 76.18 | 76.19 | 73.55 | 70.05 | 68.93 | 69.47 | 69.77 | 69.45 | 69.51
Chart: Mileage, thous.km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Standard | 1.9084 | 3.2347 | 3.3992 | 2.8426 | 2.7864 | 2.6769 | 2.5426 | 2.7435 | 2.4781 | 2.5223 | 2.323
P5 | 2.0049 | 2.4814 | 2.4012 | 2.7001 | 2.3091 | 2.5306 | 2.4438 | 2.6267 | 2.6802 | 2.6105 | 2.5012
Notes: The P5 profile is characterized by an increased level of frame forces and a lower level of the stability coefficient at the first stages of operation (up to 50-60 thousand km.). For wagons on bogies of type 18-9855, equipped with side supports of permanent contact, this is not dangerous.
For wagons with bogies of type 18-100 (without side bearings of permanent contact), it is necessary to reduce the maximum speed of movement in order to ensure compliance with regulatory requirements by a value that depends on the state of the track.
Для профиля П5 характерен повышенный уровень рамных сил и пониженный уровень коэффициента устойчивости на первых этапах эксплуатации (до 50-60 тыс. км.). Для вагонов на тележках типа 18-9855, снабженных боковыми опорами постоянного контакта это неопасно.
Для вагонов с тележками типа 18-100 (без боковых опор постоянного контакта) потребуется снижать максимальные скорости движения, чтобы обеспечить выполнение нормативных требований на величину, зависящую от состояния пути.

## Slide 31: Optimal profile for passenger cars – P9
Optimal profile P9
has significant advantages in terms of wear of flange as compared to the standard conical profiles (GOST 10791). Resource for the wear of the flange increases almost unlimited, and the wear of the tread are equivalent.
Durability for fatigue strength for the profile of P9 is 80-100 thousand km greater.
Chart: Mileage, thous.km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Standard | 0 | 0.21 | 0.35 | 0.45 | 0.54 | 0.62 | 0.7 | 0.8 | 0.9 | 1.01 | 1.12
P9 | 0 | 0.13 | 0.26 | 0.36 | 0.48 | 0.59 | 0.7 | 0.81 | 0.92 | 1.03 | 1.14
Chart: Mileage, thous.km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Standard | 0 | 1.11 | 1.54 | 1.87 | 2.14 | 2.37 | 2.6 | 2.79 | 2.94 | 3.04 | 3.1
P9 | 0 | 0 | 0 | 0.07 | 0.16 | 0.23 | 0.31 | 0.37 | 0.44 | 0.5 | 0.57
Chart: Mileage, thous.km
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Standard | 0 | 0.076 | 0.2 | 0.343 | 0.482 | 0.61 | 0.714 | 0.802 | 0.881 | 0.95 | 1
P9 | 0 | 0.035 | 0.069 | 0.113 | 0.177 | 0.247 | 0.322 | 0.399 | 0.476 | 0.557 | 0.638
Standard
Notes: These results are obtained for passenger cars with bogies such as TVZ-CNII-M with standard conical wheel profiles ГОСТ (as a basis for comparison) and optimal profile P9.
The optimum profile ensures a more even distribution of the material to be removed from the contact surface of the profile. Due to the greater conformability, the P9 profile provides a reduction in contact stress and an increase in the fatigue life of the rolling surface.
Оптимальный профиль обеспечивает более равномерное распределение удаляемого материала с контактируемой поверхности профиля. Благодаря большей конформности профиль П9 обеспечивает снижение напряжений в контакте и увеличение усталостной долговечности поверхности катания.

## Slide 32: Contents
Recent Advances in Universal Mechanism Software
  New tool for predicting wear of railway wheel profiles
  Renewed UM RCF tool
  New tool for simulation of pantograph-catenary interaction
  New graphical engine
Recently finished projects
  Optimization of wheel profiles: dynamics, wear and rolling contact fatigue
  International benchmarking of longitudinal train dynamics simulators
  Train simulator
Conclusion

## Slide 33: Introduction
  Wu, Q. International benchmarking of longitudinal train dynamics simulators: benchmarking questions / Qing Wu, Maksym Spiryagin, Colin Cole // Vehicle system dynamics. – 2017. – Vol.55(4). – P. 450-463.
  Wu, Q. International benchmarking of longitudinal train dynamics simulators: results / Qing Wu, Maksym Spiryagin, Colin Cole, Chongyi Chang, Gang Guo, Alexey Sakalo, Wei Wei, Xubao Zhao, Nico Burgelman, Pier Wiersma, Hugues Chollet, Michel Sebes, Amir Shamdani, Stefano Melzi, Federico Cheli, Egidio di Gialleonardoi, Nicola Bosso, Nicolò Zampieri, Shihui Luo, Honghua Wu & Guy-Léon Kaza // Vehicle System Dynamics. – 2018. – V.56(3). – P. 343-365.
  Wu, Q. Longitudinal train dynamics: an overview. / Qing Wu, Maksym Spiryagin, Colin Cole // Vehicle system dynamics. – 2018. – Vol.54(12). – P. 1688-1714.
  In 2016-2017 the international benchmarking of longitudinal train dynamics simulators was made. Benchmarking was initiated by the Central Queensland University, Rockhampton, Australia. Nine programs from six countries took part in the benchmarking: TABLDSS, UM, CRE-LTS, TDEAS, PoliTo, TsDyn, CARS, BODYSIM и VOCO. Background, models and results are published in the series of papers given below.

## Slide 34: Participants of the benchmark
1 Central Queensland University, Australia CRE-LTS
2 China Academy of Railway Sciences, China CARS
3 Bryansk State Technical University, Russia &
Monash University, Australia UM
4 Dalian Jiaotong University, China TABLDSS
5 DEKRA Rail, Netherlands &
Delft University of Technology, Netherlands BODYSIM
6 Institut Français des Sciences et Technologies des Transports et de l’Aménagement des Réseaux, France & Université de Technologie de
Compiègne, France VOCO
7 Politecnico di Milano, Italy TsDyn
8 Politecnico di Torino, Italy PoliTo (SIMPACK)
9 Southwest Jiaotong University, China TDEAS

## Slide 35: Source data: 4 train configurations
Configuration Specification
Train 1 2 locos + 50 wagons
Train 2 2 locos + 50 wagons +2 locos + 50 wagons
Train 3 3 locos + 240 wagons
Train 4 2 locos + 120 wagons + 1 loco + 120 wagons
4th train configuration in Universal Mechanism software
Totally 4 train configurations were considered and compared

## Slide 36: Source data: Miner SL-76 draft gear

## Slide 37: Source data: track elevation
Track elevation

## Slide 38: Source data: track curvature
Track curvature

## Slide 39: Source data: reconstructed track plan
Reconstructed track plan

## Slide 40: Source data: traction and braking characteristics
Traction characteristics
Braking characteristics

## Slide 41: Source data: driving control

## Slide 42: Simulation results: Maximum in-train forces (Train 1)
Maximum in-train forces at different wagon positions
62 kN
440 kN
Relative error:
62 / 440 = 14%

## Slide 43: Simulation results: 10th in-train force in time domain
10th in-train force in time domain (Train 1) with plots progressively shifted upwards by 200 kN
Сила в десятом межвагонном соединении от времени (конфигурация поезда 1), графики последовательно сдвинуты вверх на 200 кН

## Slide 44: Simulation results: draft gear force diagram (force vs. deflection)

## Slide 45: Simulation results: Maximum in-train forces (Train 2)
Maximum in-train forces at different wagon positions

## Slide 46: Simulation results: Maximum in-train forces (Train 3)
Maximum in-train forces at different wagon positions

## Slide 47: Simulation results: Maximum in-train forces (Train 4)
Maximum in-train forces at different wagon positions

## Slide 48: Numerical simulation: conventional and parallel Park method
Chart: Simulation time, s
| Conventional | Parallel, 1 thread | Parallel, 2 threads | Parallel, 3 threads | Parallel, 4 threads | Parallel, 5 threads | Parallel, 6 threads | Parallel, 7 threads | Parallel, 8 threads
 | 79.48 | 68.47 | 51.94 | 45.31 | 42.03 | 45.39 | 43.08 | 42.83 | 43.97
Train 1, 2 locos + 50 wagons, 52 d.o.f.
Model time: 718 s.
Simulation time for conventional and parallel Park method

## Slide 49: Conclusions
The major differences among the various simulators lie in the draft gear models. There are differences regarding modelling of pre-load, loading characteristics and transitional characteristics.
Specifically, TABLDSS, UM, TDEAS and TsDyn had an overall agreement in terms of largest in-train forces and the corresponding connection positions.
CRE-LTS reported relatively larger magnitudes for the largest tensile in-train forces than did UM, TABLDSS, TsDyn and TDEAS in Train 2 to Train 4.
CRE-LTS recorded different connection positions for the largest in-train forces in Train 3 and Train 4;
CARS has also recorded different connection positions in Train 2 and Train 3.
PoliTo and BODYSIM also produced good results when their draft gear models had stable performance.

## Slide 50: Contents
Recent Advances in Universal Mechanism Software
  New tool for predicting wear of railway wheel profiles
  Renewed UM RCF tool
  New tool for simulation of pantograph-catenary interaction
  New graphical engine
Recently finished projects
  Optimization of wheel profiles: dynamics, wear and rolling contact fatigue
  International benchmarking of longitudinal train dynamics simulators
  Train simulator
Conclusion

## Slide 51: Train Simulator by Savronik
Train simulator by Savronik company. Train simulator has Universal Mechanism as a dynamic engine.
http://www.savronik.com.tr

## Slide 52: Train Simulator
Scenario Computer
Screen
SIM 1 Screen
SIM 2 Screen
SIM 3 Screen
SIM 4 Screen
SIM 5 Screen
GSM-R
Radio
Debriefing Computer
Insructor 1
Instructor 2
http://www.savronik.com.tr

## Slide 53: Train Simulator
  Composite Train Cabin Design
  Different Locomotive / Train Set Compatible
  Radio/GSM-R Handsets
  Onboard Signalization Equipments
  Environment Camera & Microphone
http://www.savronik.com.tr

## Slide 54: Trainee’s place
  Virtual & Physical Command Controls
  LCD Panels & Touch Panel Monitors
http://www.savronik.com.tr

## Slide 55: Train Simulator
  Ability to Use Different Locomotive or Train Set
  Use of a Common Scenario with Multi Users
  Five Different Simulation Training Capability in a Class
  Easy to Use Scenario and Environmental Editor
  Use Banking/Couple Vehicles Between The Two Cabins
  9 Different Types of Locomotives
    Hyundai Rotem DMU15000
    DMU 30000
    Hyundai Rotem
    E23000
    Hyundai Rotem E68000
    ALSTOM
    DE24000
    GE
    DE33000
    TOSHIBA
    E43000
    CAF
    E65000
    FIAT
    MT5700

## Slide 56: Train Simulator
http://www.savronik.com.tr

## Slide 57: Train Simulator
http://www.savronik.com.tr

## Slide 58: Train Simulator
http://www.savronik.com.tr

## Slide 59: Contents
Recent Advances in Universal Mechanism Software
  New tool for predicting wear of railway wheel profiles
  Renewed UM RCF tool
  New tool for simulation of pantograph-catenary interaction
  New graphical engine
Recently finished projects
  Optimization of wheel profiles: dynamics, wear and rolling contact fatigue
  International benchmarking of longitudinal train dynamics simulators
  Train simulator
Conclusion

## Slide 60: Invitation to Cooperation
Software Development. We need your feedback to improve Universal Mechanism. Let us know big reports, comments, suggestions, your ideas about new tools and possibilities in UM.
Cooperation in Scientific and Applied Research: internship for PhD students, grants, papers, etc.
Contact us via
kovalev@universalmechanisn.com
um@universalmechanism.com

## Slide 61: Roman Kovalev
Thank you for your attention!
Recent Advances in Universal Mechanism Software and Finished Projects
Presenter: Dr. Roman Kovalev
Laboratory of Computational Mechanics
Bryansk State Technical University