## Slide 1: Research Report
Supervisor: Prof. Liu Linya Dr Wang Shaofeng
Oct. 18th, 2018
Research on the Influence of Three Kinds of Metro Wheel Treads on Development of Rail Side Abrasion
East China Jiaotong University
Speaker：Liu yangyu

## Slide 2: Outline
Background profile
  Development situation of side abrasion
  Review of side abrasion solutions
  Motivation of our research
UM dynamics simulation
  Subway vehicle model
  Track subsystem
  Model of creep force(Non-elliptical)
  Model of wear intensity(Archard model)

## Slide 3: Outline
Result discussion
Conclusion
Outlook

## Slide 4: Background profile-Development situation of side abrasion
Side abrasion of subway rails in several major cities in China:.
Beijing Subway Line 2、144curves、5.33mm/month(R=400m)
Shanghai Subway Line 1、6 month(R=300m)

## Slide 5: Review of side abrasion solutions
Scholars | Friction coefficient | Axle weight | Superevelation | Rail inclination | Rail grinding | Increase damping
Yu chunguang et al. |  |  |  |  |  | 
 | 0.05↓16.1%↓ | 1t↑4.8%↑ | / | / | / | /
Lu Yun | 5.33mm/month-1.3mm/quarter | / | More surplus superevelation well(Guangzhou Line5) | / | Extend life | /
Lu Wenjiao | 0.15-0.2(R<600m) | / | Deficient superevelation well | 1:40 on curves 1:20 on straight line | / | /
Zhang Hougui | / | / | / | / | / | Delay development

## Slide 6: Motivation of our research
Try to find the best metro wheel tread for delaying the development of rail side abrasion
For the safety of the train
One of the main reasons for the scrapping of the rail
Affect the service life of the rail directly

## Slide 7: Overall research plan

## Slide 8: UM dynamics simulation-Subway vehicle model
6 degrees of freedom
6 degrees of freedom

## Slide 9: Track subsystem
Track parameter
Curve radius | 300m
Superevelation | 0.12m
Rail inclination | 1:40
Rail type | CN60
Speed | 60Km/h
Irregularities | Track Spectra of German Railway Line

## Slide 10: Track subsystem
Three kinds of metro wheel treads in China : LM、DIN5573(Shanghai metro)、S1002（Guangzhou metro）

## Slide 11: Model of creep force(Non-elliptical)
Normal contact problem
  When:
  Contact spot boundary curve:
  δ determined by Boussinesq influence fuction
  Where R is the wheel radius at the contact point, h(y) is the distance between the points of profiles in x=0 plane.
Coordinate System
Contact spot shape

## Slide 12: Model of creep force(Non-elliptical)
The elastic Winkler foundation model: a assumption about proportionality between stress and interpenetration.
  where Kp is a proportionality factor.
  Where N is normal contact force.

## Slide 13: Model of creep force(Non-elliptical)
Tangential contact problem
  FASYSIM theory
  Sliding zone and adhesive zone
  Sliding zone force:
  adhesive zone force:
FASYSIM theory schematic diagram
Notes: Sliding: 蠕滑区 adhesive： 黏着区

## Slide 14: Model of wear intensity(Archard model)
Archard model
When Archard studied the wear of materials, the corresponding material wear model was proposed. It is considered that the material wear is proportional to the normal pressure and relative sliding distance in the contact spot, and inversely proportional to the hardness of the wheel-rail material:
In UM: Fd is defined as friction work A, define Kv/H as the new wear factor Kw.
So :
Notes: Da adasda

## Slide 15: Result discussion
Rail profile change diagrams (LM)

## Slide 16: Result discussion

## Slide 17: Result discussion
three stages、linear fitting、two conclusions

## Slide 18: Conclusion
Among the three metro treads, the DIN5573 tread has the longest service time. Therefore, when the repair of the wheel treads into the DIN5573 profile will help to delay the development of the rail side abrasion and vehicles are safety to drive relatively.
When the side abrasion of the rail on the subway curves is mostly about 12mm, the develpement rate of rail side abrasion when the metro tread is DIN5573 is the fastest. So, choice S1002 will be good.

## Slide 19: Outlook
A-type subway vehicle and B-type subway vehicle in China. So, we can simulate B-type subway vehicle as well.
There are so many ways to delay the development rate of rail side abrasion, what will be found if considered it comprehensive.

## Slide 20
Thank you and best wish to UM.