## Slide 1
空气弹簧建模分析与垂向特性研究
Modeling analysis and vertical characteristics of air springs
Reporting person:Xiaolei Wang
Notes: 大家好，我来自石家庄铁道大学，我的报告题目是：空气弹簧建模分析与垂向特性研究。

## Slide 2
Contents
01
02
04
传统模型与非线性模型分析
非线性模型建模方法研究
基于试验数据对非线性模型验证
03
传统模型与非线性模型仿真结果对比
Analysis of traditional models and nonlinear models
Research on nonlinear modeling method
Comparison of simulation results between traditional models and nonlinear models
Validation of nonlinear model based on test data
Notes: 在接下来里，我将主要介绍以下内容，首先介绍空气弹簧传统模型与非线性模型的区别与研究现状；在第二部分中重点介绍本文的非线性模型的建模方法及特点，这一部分是本文的核心；在第三部分介绍空气弹簧传统模型和非线性模型仿真结果的对比；第四部分介绍基于试验数据对非线性模型的准确性进行验证。

## Slide 3
01
传统模型与非线性模型分析
Analysis of traditional models and nonlinear models
PART ONE

## Slide 4
Analysis of traditional models and nonlinear models
4
通过向气囊内充放气可以保持车身在不同载荷下的工作高度保持不变，而且可以获得较低的固有频率。
具有良好的弹性特性，能够承受垂向和横向的载荷，其刚度随着载荷的增大而变大，因此在车辆承受不同载荷变化下能保持车辆的自振频率几乎不变。
空气弹簧由于其材料的特性使它具有重量轻、寿命长、吸收高频振动的能力强等优点。
It has good elastic characteristics and can withstand vertical and transverse loads. Its stiffness increases with the increase of load, so it can keep the natural frequency of the vehicle almost unchanged under different load changes.
By filling and deflating the air bag, the working height of the body can be kept unchanged under different loads, and the lower natural frequency can be obtained.
Because of its material characteristics, air spring has the advantages of light weight, long life and strong ability to absorb high frequency vibration.
空气弹簧系统的优点：Advantages of air spring system
Notes: 空气弹簧是一种缓冲振动的弹性元件，除了拥有其他弹簧共有的弹性功能外还具有新的特点，它的气囊是由带有帘线的橡胶材料组成，在柔软的橡胶密闭容器中加入空气，利用空气的可压缩性实现弹性。空气弹簧系统一般由空气弹簧气囊、附加气室以及连接两气室的节流孔组成。气囊上端有盖板，下端有活塞，因此结构较为复杂。与其他的弹簧减振元件相比，空气弹簧有以下诸多优点：

## Slide 5
Analysis of traditional models and nonlinear models
Nishimura线性空气弹簧模型是根据工程热力学方程为基础推导的垂向动力学模型，它将空气弹簧的刚度与阻尼特性等效为钢弹簧与阻尼器的串并联模式。
缺点：没有考虑空气弹簧本体与附加气室之间连接管路内的气体交换的惯性现象，因此拥有一定的局限性。
5
空气弹簧线性数学模型Linear mathematical model of air spring
Nishimura linear air spring model is the first vertical dynamic model based on engineering thermodynamic equations. It takes the stiffness and damping characteristics of air spring as a series-parallel mode of steel spring and damper.
Disadvantage: The inertia of gas exchange between the air spring body and the additional chamber is not considered, so it has certain limitations.
Notes: 由于诸多优点，空气弹簧日益广泛的应用在高速列车、城市轨道列车和高端汽车上。因此对于空气弹簧模型的建立国内外学者进行了大量的研究，例如大家熟知的Adams/Rail软件中就采用了日本人的Nishimura线性空气弹簧模型，随着高速列车的提速与飞快发展，在日益复杂的工况下，对空气弹簧的非线性特性提出了更高的要求，因此有效的建立空气弹簧非线性模型对整车的动力学仿真结果至关重要。国内外诸多学者也对空气弹簧的非线性模型开展了大量的研究工作，并建立了一系列的空气弹簧非线性模型，在此不一一介绍。本文考虑了空气弹簧的气动力学特性和非线性特性，基于Simulink建立了空气弹簧非线性模型系统，包含空气弹簧主气室子模型、附加气室子模型、节流孔方程。

## Slide 6
Analysis of traditional models and nonlinear models
6
非线性模型考虑了空气弹簧的气动力学特性和非线性特性，结合流体力学、工程热力学和空气动力学相关知识，推导出含有多个物理参数的空气弹簧状态方程，并且基于Simulink建立了空气弹簧非线性模型系统。
空气弹簧非线性气动力学模型Nonlinear aerodynamics model of air spring
In this paper, the aerodynamic and nonlinear characteristics of air springs are considered. Combined with the knowledge of hydrodynamics, engineering thermodynamics and aerodynamics, the state equation of air springs with multiple physical parameters is derived. A nonlinear model system of air springs is established based on Simulink.
Notes: 由于诸多优点，空气弹簧日益广泛的应用在高速列车、城市轨道列车和高端汽车上。因此对于空气弹簧模型的建立国内外学者进行了大量的研究，例如大家熟知的Adams/Rail软件中就采用了日本人的Nishimura线性空气弹簧模型，随着高速列车的提速与飞快发展，在日益复杂的工况下，对空气弹簧的非线性特性提出了更高的要求，因此有效的建立空气弹簧非线性模型对整车的动力学仿真结果至关重要。国内外诸多学者也对空气弹簧的非线性模型开展了大量的研究工作，并建立了一系列的空气弹簧非线性模型，在此不一一介绍。本文考虑了空气弹簧的气动力学特性和非线性特性，基于Simulink建立了空气弹簧非线性模型系统，包含空气弹簧主气室子模型、附加气室子模型、节流孔方程和分数阶模型。

## Slide 7
02
非线性模型建模方法研究
Research on nonlinear modeling method
PART TWO

## Slide 8
Research on nonlinear modeling method
8
橡胶气囊与附加空气室子模型Rubber gasbag and additional model
内部气体满足理想气体状态方程
······ (2-1)
由于振动过程中接近于工程热力学中的绝热过程
······ (2-2)
······ (2-4)
(2-3)求导
橡胶气囊
······ (2-3)
······ (2-5)
The internal gas satisfies the ideal gas equation of state.
The vibration process is close to the adiabatic process in engineering thermodynamics
Notes: 对空气弹簧悬挂系统的各个部分分别进行建模。首先是空气弹簧主气室（也就是橡胶气囊），它的内部气体满足理想气体状态方程，如式（2-1）。由于空气弹簧在振动过程中接近于工程热力学中的绝热过程，即系统与外界能量不进行交换。此时为闭口系统，根据热力学第一定律，各种形式的能量可以相互转换，在转换中数量保持恒定，当系统循环完一个周期后，其状态参数恢复原值，与外界交换的净能量为零。（空气弹簧在初始状态到任意时刻状态下是等熵过程），因此满足以下两个方程，对其求导得到内部压强变化微分方程。对于橡胶气囊而言，其涉及气体质量变化与体积变化，而附加空气室只涉及内部气体质量变化。

## Slide 9
Research on nonlinear modeling method
9
主气室与附加气室气体的进出方向相反，但是气体质量变化一定
······ (2-7)
由于附加气室是刚性的，所以固定容积不变
附加气室
······ (2-6)
(2-4)求导
节流孔子模型Throttling Confucius model
气体微元的动量守恒方程
······ (2-8)
橡胶气囊与附加空气室子模型Rubber gasbag and additional model
Because the additional chamber is rigid, the fixed volume remains unchanged
The main chamber is opposite to the gas inlet and outlet direction of the additional chamber.
Momentum conservation equation for gaseous infinitesimal
Notes: 基于空气动力学理论，在气动管路中选中一个体积为Ve的气体微元，其空间矢量为X 移动速度矢量为 V 表面法向量为n，假设气体流入节流孔的过程看做等熵流动，其运动满足动量守恒方程。（2-8）
p气体密度、森个吗为表面应力张量，f为空间场矢量、左式为气体微元动量的变化量，右一为气体微元所受的表面力、右二为气体微元所受的场力

## Slide 10
Research on nonlinear modeling method
10
节流孔流量方程
······ (2-10)
······ (2-11)
对节流孔而言，其较短且管壁较光滑，故可忽略气体微元所受的表面力和重力，且由于节流孔直径远小于管道轴线弯曲曲率，可忽略气流横向速度的影响：
由式(2-8)简化
······ (2-9)
积分
For the throttle orifice, the surface force and gravity exerted by the gas element can be neglected due to its shorter length and smoother tube wall. Because the diameter of the throttle orifice is much smaller than the bending curvature of the pipeline axis, the influence of the transverse velocity of the gas flow can be neglected.
Orifice flow equation
节流孔子模型Throttling Confucius model
Notes: 气体在节流孔中的流动可以简化为2-9，对它积分，得到2-10 式中min和max分别表示节流孔两端压力较小和压力较大的横截面。最终得到的节流孔流量方程如式2-11，通过该方程可以计算出内部气体质量变化。R为通用空气常数，n为多变指数。最终能够得到节流孔流量方程（式2-11）.

## Slide 11
Research on nonlinear modeling method
11
Simulink建立的空气弹簧模型系统Air spring model system established by Simulink Throttling Confucius model
Notes: 气体在节流孔中的流动可以简化为2-9，对它积分，得到2-10 式中min和max分别表示节流孔两端压力较小和压力较大的横截面。最终得到的节流孔流量方程如式2-11，通过该方程可以计算出内部气体质量变化。R为通用空气常数，n为多变指数。最终能够得到节流孔流量方程（式2-11）.

## Slide 12
Research on nonlinear modeling method
12
垂向刚度特性试验Vertical stiffness test
A certain type of diaphragm air spring body is placed in the center position of the free vibration table. The height of the air spring is 326mm and the upper cover plate is fixed so that the air spring can vibrate with the vibration of the vibration table.
将某型号的空气弹簧本体放置在自由振动台的中心位置，冲入气压，调整空气弹簧的高度为326mm，并且固定上盖板，使得空气弹簧能随着振动台的激振进行振动。
Notes: 通过垂向静刚度与动刚度试验对空气弹簧非线性垂向气动模型进行验证。

## Slide 13
Research on nonlinear modeling method
13
垂向刚度特性试验Vertical stiffness test
静刚度试验：在空气弹簧的底部加载频率为0.125Hz振幅为10mm的位移激振，记录载荷位移曲线。
动刚度试验：在空气弹簧底部分别加载频率为1Hz、振幅分别为5mm和10mm的位移激振，记录载荷位移曲线。
Static stiffness test: At the bottom of the air spring, the displacement excitation frequency is 0.125 Hz and the amplitude is 10 mm. The load displacement curve is recorded
Dynamic stiffness test: In the bottom part of the empty spring, the displacement excitation frequency is 1Hz, the amplitude is 5mm and the amplitude is 10mm, respectively. The load-displacement curves are recorded.

## Slide 14
03
传统模型与非线性模型仿真结果对比
Comparison of simulation results between traditional models and nonlinear models
PART THREE

## Slide 15
Comparison of simulation results between traditional models and nonlinear models
15
载荷-时间曲线Load-time curve
同等工况下，非线性模型的垂向支反力均小于传统模型，由于线性模型忽略了两气室之间的气体交换，使得支反力过大，刚度过大，模型准确性较差。而非线性模型能够较好的体现了节流孔的阻尼特性。
Under the same working conditions, the vertical branch reaction force of the nonlinear model is smaller than that of the traditional model. Because the linear model ignores gas exchange between the two chambers, the branch reaction force is too large, the stiffness is too large, and the accuracy of the model is poor. The nonlinear model can better reflect the damping characteristics of throttle orifice.
在仿真试验中，将模型的上盖板固定住，并对空气弹簧气囊冲入430Kpa和570Kpa的压强，对其下盖板施加一个频率为1HZ，振幅为10mm的正弦激励，测定两种模型的支反力F，并计算动态刚度。
Notes: 在仿真试验中，将空气弹簧非线性模型的上盖板固定住，并对空气弹簧气囊冲入430Kpa和570Kpa的压强，对其下盖板施加一个频率为1HZ，振幅为10mm的正弦激励，测定两种模型的支反力F，并计算动态刚度。

## Slide 16
Comparison of simulation results between traditional models and nonlinear models
16
静态、动态刚度对比Comparison of static and dynamic stiffness
动态加载下，传统模型与非线性模型刚度差值增大。
两种模型的空气弹簧的垂向动态刚度与工作压力大体上成正比，压力越高，载荷越大，刚度越大。
The vertical dynamic stiffness of air springs of the two models is approximately proportional to the working pressure. The higher the pressure is, the greater the load is and the greater the stiffness is.
Under dynamic loading, the stiffness difference between the traditional model and the nonlinear model increases.
Notes: 由图可知，非线性模型刚度始终小于传统模型刚度，

## Slide 17
Comparison of simulation results between traditional models and nonlinear models
17
刚度、阻尼特性Stiffness and damping characteristics
体积比：随着附加气室容积的减小，空气弹簧的刚度会大幅增大，在体积比为0.5-1.5范围内变化较为明显，当体积比大于1.8时空气弹簧的刚度变化不再明显。
动态刚度和动态阻尼特性均随着橡胶气囊体积的增加而近似线性减小
空气弹簧的动态阻尼随着附加空气室体积的增加而近线性增加
Both dynamic stiffness and dynamic damping decrease linearly with increasing airbag volume.
The dynamic damping of the air spring increases linearly with the increase of the volume of the additional air chamber.
Volume ratio: With the decrease of additional chamber volume, the stiffness of air spring will increase greatly, and the change is obvious in the range of volume ratio 0.5-1.5. When the volume ratio is greater than 1.8, the stiffness of air spring will not change obviously.
Notes: 为了进一步确定线性模型与非线性气动力学模型的差异，在同等压强和载荷工况下，保持其他参数不变，仅仅改变两气室的体积比，得出刚度与体积比的曲线图如下图所示。

## Slide 18
04
基于试验数据对非线性模型的验证
Validation of nonlinear model based on test data
PART FOUR

## Slide 19
Validation of nonlinear model based on test data
19
静刚度滞回曲线Hysteresis curve of static stiffness
随着充入内压的依次增大，垂向载荷也逐渐增大，试验结果与仿真计算吻合较好。
空气弹簧静态刚度回滞曲线与试验曲线吻合较好，误差不超过5%，表明该模型能够准确的模拟不同载荷下的空气弹簧静刚度特性。
With the increase of internal pressure in turn, the vertical load increases gradually, and the experimental results are in good agreement with the simulation calculation.
The static stiffness hysteresis curve of air spring is in good agreement with the test curve, and the error is less than 5%. It shows that the model can accurately simulate the static stiffness characteristics of air spring under different loads.
Notes: 本文按照试验工况下对空气弹簧非线性模型进行同等状态下分析，得出载荷位移曲线。

## Slide 20
Validation of nonlinear model based on test data
20
动刚度滞回曲线Hysteresis curve of dynamic stiffness
空气弹簧非线性模型仿真出的载荷位移曲线与试验特性曲线大致吻合，反映出空气弹簧非线性模型较好的描绘出动刚度特性，动刚度大小与试验结果基本相同，误差在5%以内，体现了模型的准确性。
The load-displacement curve simulated by the air spring aerodynamic model agrees with the test characteristic curve roughly, which reflects that the air spring aerodynamic model can describe the dynamic stiffness characteristics better. The dynamic stiffness is basically the same as the test results, and the error is less than 5%, which reflects the accuracy of the model.
Notes: 同理，将仿真与试验调整为同等条件下，将频率调整为1HZ，其他条件不变。

## Slide 21
Validation of nonlinear model based on test data
21
静刚度规律性Regularity of static stiffness
动刚度规律性Regularity of dynamic stiffness
压强增大，静刚度增大
载荷增大，动刚度增大
振幅增大，动刚度减小
When load increases, dynamic stiffness increases.
The amplitude increases and the dynamic stiffness decreases.
pressure increases, static stiffness increases.

## Slide 22
总结与展望 Summary and prospect
22
首先，利用工程热力学理论与空气动力学理论，推导出含有多个物理参数的空气弹簧状态方程，并且基于Simulink建立了空气弹簧非线性模型系统，对空气弹簧的非线性特性进行了深度的研究。
其次，基于Simulink建立了空气弹簧的非线性模型，仿真出载荷位移曲线、动静刚度曲线以及刚度、阻尼随着气囊体积和附加气室体积的变化规律，并对比传统的线性模型，在垂向刚度和阻尼特性上能够体现非线性模型的优越性
最后，利用试验数据对非线性模型的准确性进行验证，表明该模型能够较好的反映空气弹簧的实际垂向特性。
Firstly, the non-linear characteristics of the air spring are studied in depth by using the engineering thermodynamics theory and the air thermodynamics theory, considering the gas exchange between the main chamber and the additional chamber of the air spring.
Secondly, the nonlinear model of air spring is established based on Simulink. The load-displacement curve, dynamic and static stiffness curve, stiffness and damping varying with the volume of air bag and additional air chamber are simulated. Compared with the traditional linear model, the vertical stiffness and damping characteristics of the nonlinear model can reflect the superiority of the nonlinear model
Finally, the accuracy of the nonlinear model is verified by the experimental data, which shows that the model can better reflect the actual vertical characteristics of the air spring
Notes: 首先，利用工程热力学理论与空气热力学理论，考虑了空气弹簧主气室与附加气室的气体交换现象，对空气弹簧的非线性特性进行了深度的研究。
其次，基于Simulink建立了空气弹簧的非线性模型，仿真出载荷位移曲线、动静刚度曲线以及刚度、阻尼随着气囊体积和附加气室体积的变化规律，并对比传统的线性模型，在垂向刚度和阻尼特性上能够体现非线性模型的优越性
最后，利用试验数据对非线性模型的准确性进行验证，表明该模型能够较好的反映空气弹簧的实际垂向特性。

## Slide 23
Thanks for Your Attention