## Slide 1: Using Vehicle Simulation Modelling to Set Loading Bias Limits for Safe Operation
Dr Amir Shamdani* and Russell Bowey
Institute of Railway Technology, Monash University
(* presenting author)

## Slide 2
Presentation outline
Background (derailments and loading biases)
Derailment examples
Case study
  - Background
  - Simulation modelling
  - Results
Conclusions

## Slide 3
Flange climb derailments
Occurs when the wheel flange climbs up and over the gauge corner of the rail
We need to limit the L/V ratio!
Vertical
Lateral

## Slide 4
Flange climb derailments
Multiple contributing factors
(W/R profiles, suspension, speed, track geometry, friction, wheel position, in-train forces …)
However, often associated with:
Curves (lateral loading)
Twist (vertical unloading)
Wheel loading biases can exacerbate unloading but… derailments often destroy the evidence!

## Slide 5
Derailment examples
[ATSB, Transport Safety Investigation Report, Rail Occurrence Investigation 2007/003]
Ballast wagon (Roopena, SA)
Loading bias
Track twist
[ATSB, Transport Safety Investigation Report, Rail Occurrence Investigation 2007/003]

## Slide 6
Derailment examples
[Safety Investigation Report, Rail Occurrence Investigation 2012/004
Photo copyright, ARTC]
Ballast wagon (Broken Hill, NSW)
Loading bias
Negotiating a curve
[Cristiano Jorge et. al., ‘New Drainage Device for CVRD Iron Ore Cars’, CORE 2006]
Ore Wagon (CVRD, Brazil)
Loading bias

## Slide 7
Case study - background
Setting safe loading bias limits on empty gondola ore wagons using simulation modelling.
Wagons are emptied using rotary car dumpers
Residual ore can remain, causing a loading bias
Weighbridges are often placed just past the dumper

## Slide 8
Case study - background
The critical region of operation for derailments is the exit curve of the dumper as empty wagons are pushed during indexing
Why…?

## Slide 9
Case study - background
The critical region of operation for derailments is the exit curve of the dumper as empty wagons are pushed during indexing
Why…?
Perfect storm of contributing factors:
Tight exit curves in the yard (high L)
Empty wagons (low V) are pushed by the indexer (higher L!)
Low indexing speeds (high friction)
Limited track maintenance (production bottle neck)

## Slide 10
Case study - simulation modelling
Modelling used Universal Mechanism software with the UM Loco module.
As well as the loading bias, other factors considered during modelling were:
Wheel / rail friction
Train propelling speed
Short twist error (high-rail dip)
Gauge error (gauge widening)

## Slide 11
Case study - rolling stock
Rolling stock parameters:
IRT’s generic ore car (3-piece bogie with CCSBs)
40t compressive in-train force (from IOC results)
Wagon speed of 0.1 and 1.0m/s
Load bias of up to 15t load (at rail)

## Slide 12
Case study - track
Track parameters:
Track layout: 20m tangent, 20m transition, 80m curve
300m radius curve with 25mm superelevation
Short twist errors of 10 and 15mm
Standard gauge and 24mm gauge widening
Tangent
20 m
Transition
20 m
Curve Proper
80 m
START
Twist defect
X

## Slide 13
Case study - wheel/rail interface
Wheel / rail parameters:
New wheel profiles (lowest flange angle and shallowest flange)
Worn high and low rail profiles
Dry and lubricated conditions (friction values were based on field measurements of the gauge corner and running surface)

## Slide 14
Case study - derailment criterion
Nadal’s derailment criteria
Where :
 - is the coefficient of friction between the wheel and rail
 - is the contact angle between the wheel and rail

## Slide 15
Case study - results
Resultant L/V along the track for increasing loading biases for the base case conditions:
Wagon speed of 0.1m/s
10mm short twist
Standard gauge
Dry contact conditions
The short twist defect area shows the highest L/V (circled)

## Slide 16
Case study - results
Twist traversal

## Slide 17
Case study - results
Peak L/V for all dry contact simulations

## Slide 18
Case study - results
Peak L/V for all lubricated conditions

## Slide 19
Conclusions
Wheel loading biases have been found to contribute to wheel climb derailments
A case study illustrated the use of simulation modelling with UM to set loading bias limits for lightly loaded ore cars
The case study showed that lubrication results in higher L/V ratios but safer operation since the corresponding L/V limit is also higher (using the base case the allowable bias limit could increase from 3.5t to 12t with lubrication). Lubrication could be used to permit a higher loading bias if reducing the bias proves technically difficult

## Slide 20
Conclusions
Short twist (in the form of a high-rail dip) had the most significant effect on the results. Tighter maintenance standards could be set to allow higher bias limits
Varying the speed from 0.1 to 1.0 m/s had little difference in permitted loading bias in both the lubricated and dry conditions. This covers the full range of indexing speeds
In this case study, gauge widening had a beneficial effect on the L/V. Therefore, any apparent gauge widening due to gauge face wear should not increase the risk of derailment

## Slide 21
Thank you!