## Slide 1: Floating Slab Track Parameter Optimum Design Based on TMT’s Systematic Method
IV International Scientific and Technical Workshop
“Computer simulation in railway transport: dynamics, strength, wear”
LIU Wei1, LIU Zhen-guang1, BU Ji-lin1, LEI Qiang2
1. CRRC Zhuzhou Times New Material Technology Co., Ltd, China
2. Sichuan Tongsuan Technology Co., Ltd, China
April 3, 2018, Bryansk State Technical University, Russia
Notes: Dear Professor Pogorelov, dear colleagues, dear friends, hello every one. My name is John, come from China. Actually, I’m not a scientific researcher. I just sell Universal Mechanism in China. Now there are more than 10 paid users in China. Today, it’s my honor to be present here to make the presentation on behalf of the UM user CRRC TMT in China. The topic is Floating Slab Track Parameter Optimum Design Based on TMT’s Systematic Method. The research work has been finished by my customer and friends, Dr. Liu Wei and his colleagues, with help of the software Universal Mechanism, which I sold to them 2 years ago.

## Slide 2: 目 录
ONTENTS
C
Company Profile
Optimum Method
Research Background
Notes: Firstly, I would like to briefly introduce the authors’ company, then the background for the research project, and then what they did.

## Slide 3
1
CRRC
CRRC is one of the largest manufacturers in rail transit industry.
CRRC has 46 subsidiaries around the world and more than 180,000 employees.
CRRC produces almost all types of railway vehicles and equipment, including locomotives, passenger cars, freight wagons, high-speed trains, metro vehicles, monorail and maglev vehicles.
Company Profile
Notes: CRRC is one of the largest manufacturers in rail transit industry. You may know some other famous companies in this filed, such as SIEMENS, ALSTOM, BOMBARDIER, and Kawasaki. CRRC now has 46 subsidiaries around the world and with more than one hundred eighty thousand employees. CRRC produces almost all types of railway vehicles and railway equipment, including locomotives, passenger cars, freight wagons, high-speed trains, metro vehicles, monorail and maglev vehicles.

## Slide 4
Industry Ranking
The world’s largest manufacturer of elastic components for rail transit .
Top 15 of world’s non-tire rubber manufacturing industry, and No.1 in China.
Company Profile
TMT is a subsidiary of CRRC and specialized in polymer and composite materials research and engineering applications.
TMT is a leading supplier for the development, production and sales of NVH components and polymer composite materials for the railway, automotive, construction , wind power as well as special equipment industry.
TMT’s products cover 30 Countries and regions.
More than 500 customers and suppliers domestic and overseas.
The best supplier/strategic partner of Bombardier Inc, GE Inc, Alstom Inc and so on.
Corporate Customers
1
CRRC TMT
Page 4
Notes: And TMT is one of the subsidiaries of CRRC, which is specialized in polymer and composite materials research and engineering applications. TMT is a leading supplier for the development, production and sales of NVH components and polymer composite materials for the railway, automotive, construction, wind power as well as special equipment industry. Now it is the world’s largest manufacturer of elastic components for rail transit. In the non-tire rubber field, it ranks top 15 in the world and top 1 in China. The products of TMT have covered 30 countries and regions, with more than 500 customers in the world. It is one of the best suppliers for BOMBARDIER, GE and ALSTOM.

## Slide 5
1
Products of TMT
For vehicle
For bridge
For wind
Notes: Here, you can see the main products of TMT, these elastic components are used for automotive, railway vehicle, bridge and wind power.

## Slide 6: 目 录
ONTENTS
C
Company Profile
Optimum Method
Research Background
Notes: OK, the second part of my presentation, research background.

## Slide 7
2
Traffic jam
More and more people move to big cities for work, which makes traffic jam every day
Notes: In China, more and more people go to big cities for job, study or tour. Such as Beijing, Shanghai, Shenzhen, Guangzhou, and Chengdu. The traffic jam happens almost every day.

## Slide 8
2
Metro transit
Notes: So these big cities decided to construct metro lines in order to relieve the crowded traffic. Here I show you the metro map of Beijing, now there are 20 metro lines. While 10 years ago, there were only 3-5 metro lines. As far as I know, about 30 cities in China are constructing metro lines.

## Slide 9
2
Vibration and noise
How to decrease noise and vibrations caused by wheel-rail contact?
Notes: As we know, a metro line often goes through underground, which may cause two main problems, vibration and noise. Scientists and engineers try to decrease the noise and vibrations, which caused by wheel-rail contact.

## Slide 10
2
Floating slab
Will the floating slab works?
How to find the optimum parameters of stiffness and damping of fasteners?
What is the proper step size for slab springs?
Notes: One of the effective methods is to equip so called Floating Slab between the rail and foundation. You can see some pictures of Floating Slab. Elastic fasteners connect the rail and floating slab, and between the floating slab and the foundation, there are springs. So, there may be some technique questions. Will the floating slab works? How to find the optimum parameters of stiffness and damping of fasteners? And what is the proper step size for slab springs?

## Slide 11: 目 录
ONTENTS
C
Company Profile
Optimum Method
Research Background
Notes: Now let us move to the last part: Optimum method.

## Slide 12
Rail Parameters
Vehicle vibration
Rail vibration
Slab vibration
Wheel-rail force
Fastener force
Spring force
Optimized Parameters
Vehicle Dynamics
Rail Dynamics
Slab Dynamics
Wheel/Rail
Interaction
Rail/Slab
Interaction
Vehicle Parameters
Slab Parameters
3
Optimum method
Notes: About 4 years ago, the company TMT proposed a so called systematic method. They would like to create the whole dynamic system of vehicle, rail, slab and including elastic components, even including bridges or tunnels. In this system, both wheel/rail contact and flexible rail/slab interaction are taken into account. Then they can get the dynamics responses of vehicle, rail, slab, fastener and spring. According to some index, they can modify and optimize some parameters of the track slab system.

## Slide 13
UM Loco
UM FEM
UM Flexible Railway Track
Training course in TMT, 2016
3
Simulation tool
Notes: From 2014 to 2015, the TMT Company investigated many softwares all around the world, they also set up a benchmark for it. As a result, they regarded Universal Mechanism should be the best one and chose it. Some main modules should be used, UM Loco, UM FEM and UM Flexible Railway Track. Here is a photo, that I gave training course to TMT in 2016. The man stands on my right side is the first author, Dr. Liu Wei, who graduated from Southwest Jiaotong University in Chengdu.

## Slide 14
Transition section
Standard section
Additional spring
3
Dynamics model
Standard section
Transition section
Transition section
Rigid vehicle（UM）
Flexible rail（UM）
Flexible slab（ANSYS）
Notes: After my training, Dr. Liu Wei and his colleagues started some research projects with the help of UM software. In this slide, it shows one of their models, which consists of rigid multi-body vehicle, flexible rail and flexible floating slab. I’m sorry the image of rail is hidden in these pictures. The fasteners can be created by bushing force element automatically, and the springs between floating slab and foundation can only be added manually.

## Slide 15
3
Dynamics response: vertical wheel-rail force
Notes: At last, I would like to show you some simulation results. Here you see, different types of fasteners may lead to different vertical wheel-rail forces.

## Slide 16
3
Dynamics response: lateral wheel-rail force
Notes: And different lateral wheel-rail forces.

## Slide 17
3
Dynamics response: fastener force
Notes: And different reaction forces of fastener.

## Slide 18
3
Dynamics response: vertical slab acceleration
Notes: The damping coefficient of fastener did influence the vibration of floating slab in vertical direction.

## Slide 19
3
Dynamics response: lateral slab acceleration
Notes: And in lateral direction.

## Slide 20
3
Dynamics response: vertical rail displacement
Notes: Also the displacement of rail.

## Slide 21
3
Dynamics response: vertical rail acceleration
Notes: The acceleration of rail. They also did some experiments, but currently these data is still kept in secret because of commercial competition. During the research project, they got optimum values for stiffness and damping coefficient of fasteners, and step size of slab springs. So the conclusion is that their choice of Universal Mechanism is absolutely correct.

## Slide 22
2018-04-03
Thank you!
Notes: Thank you for listening. Спасибо ！