## Slide 1
A vehicle-bridge interaction dynamic system analysis method based on inter-system iteration
Zhang Nan and Zhou Shuang
Beijing Jiaotong University
Bryansk, Russia, 2018-04-03
Notes: <number>

## Slide 2
Introduction
The vehicle-bridge interaction system
wind
Earthquake, settlement
Scouring
Deformation of track
Structure damage
Collision
Deformation of track: i
Wind: Fv、Fb
Collision：Fb
Structure damage: Kb
Scouring: Kb
Earthquake, settlement: Xb

## Slide 3
Introduction
Questions for vehicle-bridge interaction system
  Is the train in danger when running through a bridge?
  Is the passenger discomforted when running through a bridge?
  Is the bridge under the obvious problem of fatigue?
  Required by the bridge designing codes.

## Slide 4
Method
Models for vehicle and bridge
Elastic spring
Viscous damper
Multi-body dynamics model
In vertical / normal:
Corresponding assumption
Hertz contact theory
In lateral / tangent
Hunting assumption
Kalker linear creep theory

## Slide 5
Method
Vehicle-bridge interaction equations
Wheel-rail relation
Substituted by the wheel-rail relation

## Slide 6
Method
Inter-history iteration

## Slide 7
Method
Step1: To solve the vehicle by assuming the bridge is rigid, using the track irregularities as the excitation, to obtain the time histories of wheel-rail forces for all wheel-sets;
Step 2: To solve the bridge by applying the wheel-rail force histories on bridge deck, to obtain the updated time histories;
Step 3: To solve the vehicle by combining the updated bridge deck movements obtained in Step 2 with the track, to obtain the updated time histories of wheel-rail forces;
Step 4: To calculate the errors, if the errors for all wheel-sets in the whole history small enough, the convergence check is OK; otherwise return to Step 2 to start a next iteration loop.

## Slide 8
Case study
Case
  CRH2 train, 8 vehicles, MTMTTMTM, 300km/h
  31.5m simply-supported beam, 10 spans, without piers
  Mid span section
  Track irregularity: German Low Disturb Spectrum

## Slide 9
Case study
Method1 (ISI)
  Inter-history iteration
  Bridge model by ANSYS
  Vehicle model by UM
  Wheel-rail relation by DRVB (by my research group)
    Transferring UM w/r force into ANSYS command text
    Transferring ANSYS displacement into irregularity data for each wheel-set in UM
Method 2 (UM)
  UM, non-mass track (Hertz contact and Kalker linear creep)

## Slide 10
Case study
Mid span vertical displacement (left ISI, right UM)
Mid span vertical acceleration (left ISI, right UM)

## Slide 11
Case study
Car body vertical acceleration (left ISI, right UM)
Car body lateral acceleration (left ISI, right UM)

## Slide 12
Case study
Vertical wheel-rail contact force (left ISI, right UM)
Lateral wheel-rail contact force (left ISI, right UM)

## Slide 13
Case study
Derailment factor (left ISI, right UM)
Offloading factor (left ISI, right UM)

## Slide 14
Discussion
For the calculation of vehicle-bridge interaction
  The model of bridge?
  The time step used in calculation?
  The track structure considered?
  The safety criteria?
  The effect of longitudinal movement?
For UM
  Adoption of other software?
  Report in standard format?

## Slide 15
Thank you 谢谢 Cпасибо