## Slide 1
Simulation of pantograph-catenary interaction in «Universal Mechanism» software
Dmitry Pogorelov, Gennady Mikheev, Alexander Rodikov
Laboratory of Computational Mechanics
Bryansk State Technical University
Announcement: new module development
Моделирование взаимодействия пантографа с контактной сетью в ПК "Универсальный механизм"

## Slide 2
UM Catenary
In 2018 we have started the development of a new module UM Catenary

## Slide 3
Pantograph-Catenary interaction software
(1) DB – DB Systemtechnik GmbH (PrOSA), Germany; (2) IST – Instituto Superior Tecnico Lisboa (PantoCat), Portugal; (3) KRRI – Korea Railroad Research Institute (SPOPS), Republic Korea; (4) KTH – Royal Institute of Technology (CaPaSIM), Sweden; (5) POLIMI – Politecnico di Milano (PCaDA), Italy; (6) RTRI – Railway Technical Research Institute (Gasen-do FEM), Japan; (7) SNCF – Societé Nationale des Chemins de Fer (OSCAR), France; (8) SWJTU – Southwest Jiaotong University (PCRUN), People’s Republic of China; (9) UPCo – Universidad Pontificia Comillas de Madrid (CANDY), Spane; (10) UPV/TALGO – Universitat Politècnica de València & TALGO S.L. (PACDIN), Spane.
World-wide scientific activities in simulation of railway catenary system dynamics
Benchmarking:
Stefano Brunia, Jorge Ambrosiob, Alberto Carniceroc, Yong Hyeon Chod, Lars Finnere, Mitsuru Ikedaf, Sam Young Kwond, Jean-Pierre Massatg, Sebastian Stichelh, Manuel Turi and Weihua Zhang. The results of the pantograph–catenary interaction benchmark. Vehicle System Dynamics, 2015, Vol. 53, No. 3, Pages 412–435.

## Slide 4
UM Catenary
Types of railway catenary systems to be implemented:
Simple
Switched
Compound

## Slide 5
Model of 3D catenary system
Main elements:
Messenger wire: geometric nonlinear beam elements (developed by our team for simulation of drill strings) or tensioned beam FE
Contact wire: tensioned beam FE
Droppers: bipolar force elements

## Slide 6
Analysis of catenary systems
Tests:
Equilibrium of catenary system:
Given vertical positions of contact wire at dropper locations and wire tensions
Dynamic analysis of pantograph-catenary system interaction
Pantograph only
Complete 3D model of locomotive

## Slide 7
Equilibrium test
Example: 4 spans, 220 meters, 80 geometrically nonlinear FE
Equilibrium computation by integration of motion equations
Simulation is 10 times faster than real time

## Slide 8
Simulation of pantograph-catenary interaction in «Universal Mechanism» software
Dmitry Pogorelov, Gennady Mikheev, Alexander Rodikov
Laboratory of Computational Mechanics
Bryansk State Technical University
Моделирование взаимодействия пантографа с контактной сетью в ПК "Универсальный механизм"
The module will be available for distribution in 2018