## Slide 1
G.V. Mikheev, S.B. Tomashevskiy
Bryansk State technical university, Laboratory of computational mechanics, bulvar 50 let Oktyabrya 7, 241035 Bryansk, Russia e-mail: mikheev@umlab.ru, tomashevskiy@umlab.ru www.universalmechanism.com
um fea – new tool for the preparation of elastic subsystems in um software
3-4 April 2018, Bryansk, Russia
IV scientific and technical seminar
Computer simulation in railway transport: dynamics, strength, wear

## Slide 2
UM FEM
UM FEM – simulation of dynamics of flexible bodies which undergo arbitrary three-dimensional motion. Flexible displacement over deformations are considered as small one
Examples of objects of studies using the UM FEM
Diesel locomotive TEM21 with flexible bogie frame
Long-wheelbase flatcar with flexible frame
Railcar AC4 with elastic body

## Slide 3
UM FEA
UM FEM
import of data from finite element analysis software
Purpose of the module UM FEA
Development of finite element models for dynamic analysis in the UM on the basis of a modal approach, calculation of natural frequencies and forms, static analysis.
Application area of the module UM FEA
Models of the standard designs which are used generally in rolling stock which can be received by rotation or translation of flat mesh.
ANSYS
NX NASTRAN
MSC.NASTRAN
ABAQUS
UM FEA

## Slide 4
Finite element library
Volumetric finite elements
Rigid element
Shell finite elements
ζ
1
2
3
4
5
6
7
ξ
η
8
1
2
3
4
5
6
ξ
1
2
3
4
independent node
dependent nodes
2
3
1
Z
Y
X
Z
Y
X

## Slide 5
Window of the module UM FEA
Main menu
Model tree
Toolbar
Data inspector
Status bar
Graphics window

## Slide 6
Window of the module UM FEA
Types of tasks to be solved

## Slide 7
Application diagram of UM FEA
Preparing a geometric design model in GMESH
Preparation of finite element model of the structure in GMESH
Library of finite element models of standard details of railway rolling stock (wheels, axles, wheelsets, rails, etc.)
Import of the finite element model in UM FEA
Formation of the settlement model
Determination of material properties
Choice of interface nodes
Creation of rigid elements
Determination number of your own forms and the type of mass matrix
Calculation of static and eigenmodes and the associated matrices in accordance with the component mode synthesis method
Analysis of the results of calculations in the graphics window, the formation of the input file.fum of the elastic subsystem to load data into a dynamic model of the mechanical system

## Slide 8
Creating a finite element model
Creating a geometric model
Creating a finite element model in GMESH
Importing a geometric model
(*.igs, *.stp, *.stl и др.)

## Slide 9
Application UM FEA for modeling stresses in the wheelset
Finite element model
of the wheelset
Dynamic model of the railcar
Stress distribution in
the wheelset in the movement process
of railcars

## Slide 10
Conclusion
Currently, the following works are underway to prepare for the release of the first version of the UM FEA module:
Development of a 4-node shell finite element.
Testing of algorithms implemented in the um FEA module for solving practical problems.
Filling of library of finite element models of standard details of railway rolling stock.
Preparation of reference documentation for the UM FEA module.

## Slide 11
Thanks for your attention!
um fea – new tool for the preparation of elastic subsystems in um software
G.V. Mikheev, S.B. Tomashevskiy