## Slide 1
optimization of wheel profiles by minimal wear criterion
Alexander Rodikov*, Dmitry Pogorelov, Vitaly Simonov
*e-mail: rodikov@umlab.ru

## Slide 2: Contents
Technique of prediction wear of wheel profiles in UM software
Application to optimization of wheel profiles by minimal wear criterion

## Slide 3: Approaches to wear simulation
Approaches to wear simulation
Parallel
The mutual affect of wear processes and vehicle dynamics is taken into account, i.e. small changes in the profile geometry due to wear occur directly in the dynamic integration loop.
Sequential
Does not take into account the effect of the change of the profile geometry due to wear on the vehicle dynamics – the profile geometry updates after the dynamics simulation. To obtain measurable wear, sequential simulation must be performed quite a large number of times.
1
2
3
Scheme of parallel approach of wear simulation
wear step
1

## Slide 4: Models of wheel/rail contact
2
Are suited for wear simulation
Hertzian contact theory + FASTSIM
Kik-Piotrowski contact model + modified FASTSIM
CONTACT library
Example of the contact of worn profiles: Kik-Piotrowski model

## Slide 5: Wear models
x
y
3
Fleisher model
where is the volume wear [m3];
is the wear coefficient [m3/J];
is the work of frictional forces [J].
where is the power of frictional forces [W].
where is the tangential traction [Pa];
is the sliding velocity [m/s];
is the contact patch area [m2].
While using the FASTSIM-like algorithms, the work of frictional forces is calculated according to the following formula:
where is the longitudinal wheelset velocity [m/s];
is the integration time step size [s]; is the creepages [-].

## Slide 6: Wear models
4
Specht model
where is the critical power density of frictional forces [W/m2];
is the jump coefficient [-].
mild wear regime,
W [μg/ mm2]
severe wear regime,
A [J/ mm2]
100
200
300
0
10
20
30
40
30

## Slide 7: Wear models
5
Archard model
where is the wear coefficient [-];
is the normal force [N];
if the sliding distance [m];
is the hardness of the softest contacting surfaces [N/m2];
is the normal pressure [Pa].
Sliding velocity [m/s]
Contact pressure [GPa]
Wear coefficient map

## Slide 8: Wear control parameters of wheel and rail profiles
6
  Sd is the flange thickness, measured from wheel tape-circle;
  Sh is the flange height;
  qR is the flange steepness;
  Tw is the tread wear;
  St is the flange thickness, measured from flange vertex;
  dSd, dSt are difference of parameters Sd and St between worn and initial profiles.
is the vertical rail head wear; is the lateral rail wear;
is the gauge corner wear
Note:
UM has tools for calculating of wear control parameters of profiles. The third-party software (e.g., MiniProf) for the analysis of worn profiles is not required.

## Slide 9: Profile-updating algorithm
before wear step
Histogram of distribution of volume wear along profile (w)
after wear step
wear step
1
Accumulation of volume wear for every separate wheel of wheelset
Rolling direction
Integration step
7
Wear mask

## Slide 10: Profile-updating algorithm
2
Scaling volume wear according to the mileage assigned to one wear step
3
Weighted summation of volume wear for each wheel
where , are the statistical weights of configuration and speed respectively;
is the accumulated volume wear for configuration at running speed ;
is the number of configurations;
is the number of -configuration speeds.
8
4
Calculation of wear depth in the center of each circumferential strip
where is the smoothed distribution of the volume wear;
is the arc-coordinate of the center of the strip ;
is the wheel radius;
is the width of wear accumulation interval.

## Slide 11: Profile-updating algorithm
Forward route
FL
FR
RL
RR
5
Profile updating
where is the external normal for the wheel profile.
9
Averaging (symmetrizing) of wear
Averaging wear of wheel of same wheelset
where is the wheelset index.
Averaging wear of wheelsets
where is the number of wheelsets.
3
*
Backward route
RR
RL
FR
FL

## Slide 12: Profile-updating algorithm
Comparison of simulation results of complete and simplified sets of configurations. The "simplified set" is the set of configurations with only right curves and forward routes, but with wear symmetry is taking into account.
10

## Slide 13: Parallel computations on multi-core processors
Test set of configurations
Curve radius [m] | Speeds [km/h] | Traction [-]
323 | 25, 50, 65 | 0/0.6
581 | 25, 50, 65 | 0/0.6
1497 | 25, 50, 65 | 0/0.6
 | 25, 50, 65 | 0/0.6
Total number of computations |  | 24
Curve radius [m] | Speeds [km/h] | Traction [-]
323 | 25, 50, 65 | 0/0.6
581 | 25, 50, 65 | 0/0.6
1497 | 25, 50, 65 | 0/0.6
 | 25, 50, 65 | 0/0.6
Total number of computations |  | 24
Class 2ES10 electric freight locomotive. The loco model includes 37 bodies with 110 DOF.
11

## Slide 14: Parallel computations on multi-core processors
Simulation of vehicle dynamic on one wear step
Master thread
Barrier
Task manager
Profiles update
Thread 1
Thread 2
Thread 3
Thread N
…
Fork-join model of parallel computation of wheel profiles wear
12
*Intel Core i7-12700KF CPU, 3.6 GHz, 64 GB RAM

## Slide 15: Contents
Technique of prediction wear of wheel profiles in UM software
Application to optimization of wheel profiles by minimal wear criterion

## Slide 16: Optimization of wheel profiles by minimal wear criterion
Objective function to minimize the wheel wear:
Constraints: derailment coefficient, maximum wheel-rail lateral forces, minimum critical speed.
Iterative algorithm for selecting the optimal profile
1
Selection and parameterization a start profile. Parameterization of the profile by circular arcs is used.
L
, are starting and ending slopes;
, , are radii of arcs;
, are slopes of arcs;
is the tangent length.
Note:
Not all parameters are independent, between some of these parameters there are relationship. For example, are set , , , , and values, then and values are calculated.
Optimization region
13

## Slide 17: Optimization of wheel profiles by minimal wear criterion
2
Set of profile-candidates is generated by varying the parameters in valid ranges.
3
Compared of profiles-candidates in wear simulation. Optimal profiles with minimum of the wear control parameters are selected.
4
Checking selected profiles for constraints satisfaction.
5
New iteration of profile optimization – go to step 2 and generation of the new set of profiles with decrease increment of parameters.
14

## Slide 18: Optimization of wheel profiles by minimal wear criterion
Standard profile
Optimal profile
56%
Critical value of flange wear
15

## Slide 19
optimization of wheel profiles by minimal wear criterion
Thank you for your attention!