## Slide 1
MULTIBODY SIMULATION BENCHMARK FOR DYNAMIC VEHICLE-TRACK INTERACTION IN SWITCHES AND CROSSINGS
Alexander Rodikov
e-mail: rodikov@umlab.ru

## Slide 2
Introduction
Benchmark description
Results
Conclusions and future work
Contents

## Slide 3
Introduction
List of benchmarks of railway multibody dynamics software:
1998 Manchester benchmarks for rail vehicle simulation
2008 Manchester contact benchmark
2015 Pantograph-catenary interaction benchmark
2017 International benchmarking of longitudinal train dynamics
2021 Vehicle-track interaction in switches and crossings benchmark
In 2020-2021 the international benchmarking of vehicle-track interaction in switches and crossings was made. Benchmarking was initiated by the University of Huddersfield (Huddersfield, UK) and CHARMEC (Chalmers University of Technology, Göteborg, Sweden). Nine programs took part in the benchmarking: GENSYS, MEDYNA, MUBODyn, NUCARS, SDITT, Simpack, Vampire, VI-Rail and VOCO.
1

## Slide 4
Benchmark description
2
Two different designs of turnouts and two routes are considered
Turnouts specification
Turnout | Rail | Radius [m] | Crossing angle | Max speed [km/h]
60E1-R760-1:15 | 60E1 | 760 | 1:15 | 80
56E1-R245-1:9.25 | 56E1 | 245 | 1:9.25 | 43
Through route
Diverging route

## Slide 5
3
Example of source data: sets of profiles for the switch (left) and crossing (right) of the 60E1-R760-1:15 turnout
Benchmark description

## Slide 6
Benchmark description
4
Simulation cases*
Run | Turnout | Panel | Route | Speed [km/h]
1 | 56E1-R245-1:9.25 | Switch | Through | 100
2 | 56E1-R245-1:9.25 | Switch | Diverging | 43
3 | 60E1-R760-1:15 | Switch | Through | 160
4 | 60E1-R760-1:15 | Switch | Diverging | 80
5 | 56E1-R245-1:9.25 | Crossing | Through | 100
6 | 56E1-R245-1:9.25 | Crossing | Diverging | 43
7 | 60E1-R760-1:15 | Crossing | Through | 160
8 | 60E1-R760-1:15 | Crossing | Diverging | 43
*Facing traffic is considered only

## Slide 7
5
Benchmark description
Vehicle model: passenger coach from Manchester benchmarks
S1002 wheel profile
Co-running (moving) track model
Accurate separate modelling of switch and stock rails

## Slide 8
6
Benchmark description
Benchmark variables
Var. | Description
10, 11, 12 | Total vertical, lateral and longitudinal w/r contact forces for given w/r pair
13, 14, 15 | Lateral position on rail profile for contact points 1, 2 and 3 (cp1, cp2, cp3)
16, 17, 18 | Contact patch area for cp1, cp2, cp3
19, 20, 21 | Contact angle for cp1, cp2, cp3
22, 23, 24 | Longitudinal creep for cp1, cp2, cp3
25, 26, 27 | Lateral creep for cp1, cp2, cp3
28, 29, 30 | Spin for cp1, cp2, cp3
31, 32, 33 | Longitudinal tangential creep force for cp1, cp2, cp3
34, 35, 36 | Lateral tangential creep force for cp1, cp2, cp3
40, 41, 42 | Normal contact force for cp1, cp2, cp3

## Slide 9
7
Results
Run 2: Switch of 56E1-R245-1:9.25 turnout
Run 5: Crossing of 56E1-R245-1:9.25 turnout

## Slide 10
Results
8
Run 2: Total lateral w/r contact forces acting on the switch and stock rails
[kN]
Vi-Rail
Simpack
UM
Distance [m]

## Slide 11
9
Results
Run 2: Total vertical w/r contact forces acting on the switch and stock rails
Vi-Rail
Simpack
UM
[kN]
Distance [m]

## Slide 12
10
Results
Run 5: Total lateral w/r contact forces acting on crossing
Vi-Rail
Simpack
UM
Distance [m]
[kN]

## Slide 13
11
Results
Run 5: Total vertical w/r contact forces acting on crossing
Vi-Rail
Simpack
UM
Distance [m]
[kN]

## Slide 14
Conclusions and future work
Refinement longitudinal interpolation of the geometry of rail profiles
[kN]
Distance [m]
Run 5: Total vertical w/r contact forces acting on crossing
Reference profiles
12

## Slide 15
Conclusions and future work
13
Refinement track model taking into account switch rail / stock rail coupling
Switch rail
Stock rail
Preparation of user manual and models for end users

## Slide 16
MULTIBODY SIMULATION BENCHMARK FOR DYNAMIC VEHICLE-TRACK INTERACTION IN SWITCHES AND CROSSINGS
Thank you for your attention!